## Slide 1: Coaxial-type resonant power transformer
Inventors: Seunghun Baek, S. Bhattacharya
Date: Dec. 13. 2011

## Slide 2: Technology Overview
The effect of parasitic components becomes significant and unpredictable in conventional fashion as the operating frequency increases. More accurate tuning and low parasitic effects are desirable.
Overview:
High frequency operation is necessary in power conversion for high power density and downsizing of power convertor applications.
Downsizing and weight reduction are main obstacles of diffusion of promising power conversion applications, such as Electric Vehicles (EV), Solid-State Transformer (SST) etc.

## Slide 3: Technology Overview
Overview , Con’t:
Resonant conversion using soft-switching is one of the most popular techniques to increase operating frequency in high power capacity.
Cp
Resonant tank
Ls
HF transformer
Galvanic isolation using an isolation transformer in high power equipments is necessary.

## Slide 4: Technology Overview
Cross sectional view and B and E field distribution
+
The invention, the coaxial resonant power transformer (CRT), plays roles of not only an step-up or down isolation transformer but also a resonant tank, which is the heaviest and bulkiest part of power converter applications.
The CRT may incorporate the resonant tank formed by series inductance Ls and shunt capacitance Cp into its design; such integrated transformer can avoid unpredictable high frequency response and minimize the size over discrete realizations.
I

## Slide 5: Technology Overview
Core
I
Ip
Is
Core
Winding
Ip
Is
I
Winding
Coaxial type transformer
- Very low parasitic components
- Accurately predictable high frequency response
- Ideal geometry from electrical and thermal insulation point of view

## Slide 6: Technology Overview
Conductor layers (Cp)
Outer winding
Inner winding
Inner Cores (Ls)
Outer Cores
Equivalent circuit

## Slide 7: Technology Overview: Key Features and Benefits
High power density
Compact size
Easy packaging
High Frequency Power Conversion
Simple geometry and configuration
Resonant tank integration
Predictaible and stable HF response
Excellent performance of electrical and thermal insulation

## Slide 8: Potential Applications
Solid-State-Transformer, electric vehicles Etc.
Best fit for high frequency resonant converters which demand high efficiency and compact size by fine tuning of resonance.
Any power conversion application which requires galvanic isolation with high power density .

## Slide 9: Problem Statement and value proposition
The effect of parasitic components has to be mitigated and passive bulky magnetic and electric passive components
High frequency operation is necessary in power conversion for high power density and downsizing of power convertor applications.
Size reduction : Discrete magnetic and electric passive components can be eliminated by integration into the isolation transformer
Stable and predictable high frequency operation : Parasitic components are minimized
Congested electric stress and heat can be avoided.
Good electrical insulation and thermal performance is desirable

## Slide 10: Economic Impact
Are you able to quantify the financial impact of your invention? (Ex: Saves $X, or is X% more efficient)
  Will be more efficient and enable power conversion at high power and high frequency
  Typically 1%-3% more efficient power conversion

## Slide 11: Inventorship/Ownership Issues
No inventor / ownership issue
The invention was done by Seunghun Baek and Subhashish Bhattacharya

## Slide 12: Public Disclosure Issues
List any papers or public disclosures
  ECCE 2011 in Sept 2011

## Slide 13: Recommended Next Actions
Asking for IPPF to be applied to your invention?
  YES
Seeking innovation champion?
  YES